## Slide 1
Self-Driving Car Simulator
End-to-End Autonomous Driving via Behavioral Cloning
Student: Muhammad Saim Razzaq | Ahsan Nadeem
Tool: TensorFlow · Colab · Udacity Sim
Year: 2026
Inspired by NVIDIA — Bojarski et al. (2016)
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
1 / 10

## Slide 2
Project Overview
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
2 / 10
What is this project?
This project implements an autonomous driving system using deep learning. A Convolutional Neural Network (CNN) is trained — via behavioral cloning — to predict steering angles directly from raw camera images, with no hand-crafted rules.
🧠 Behavioral Cloning
Learn to drive by imitating human demonstration data
📷 End-to-End Learning
Raw pixels → steering angle No separate lane detection
☁️ Colab + Local Deploy
Train on GPU in the cloud Run in real-time locally
Platform: Udacity Self-Driving Car Simulator • Architecture: NVIDIA-inspired CNN

## Slide 3
System Workflow
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
3 / 10
1
Data Collection
Drive manually in Training Mode
▶
2
Data Balancing
Cap over-represented steering angles
▶
3
Augmentation & Prep
Pan, zoom, flip, YUV + normalize
▶
4
Train CNN (Colab)
10 epochs on GPU runtime
▶
5
Export model.h5
Download weights to local machine
▶
6
Autonomous Driving
drive.py serves steering in real-time
Training runs on Google Colab (cloud GPU) | Inference runs locally via Socket.IO on port 4567

## Slide 4
Model Architecture — NVIDIA-Inspired CNN
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
4 / 10
Input 66 × 200 × 3 (YUV)
↓
Conv 1 24 filters 5×5 /2 ELU
↓
Conv 2 36 filters 5×5 /2 ELU
↓
Conv 3 48 filters 5×5 /2 ELU
↓
Conv 4 64 filters 3×3 ELU
↓
Conv 5 64 filters 3×3 ELU
↓
Flatten
↓
Dense 100 ELU
↓
Dense 50 ELU
↓
Dense 10 ELU
↓
Output 1 — Steering angle
Key Design Decisions
ELU Activation
Avoids dying-neuron problem; smoother gradients for regression
Strided Conv
Downsamples spatial dimensions without pooling layers
Single Output
One neuron predicts continuous steering angle (regression task)
End-to-End
No hand-crafted features — network learns road cues from data
Input: YUV
YUV colour space separates luminance for better light invariance
MSE Loss
Mean Squared Error is ideal for continuous steering prediction

## Slide 5
Data Processing & Augmentation
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
5 / 10
Preprocessing Pipeline
1
Crop
Remove sky & car hood → rows 60:135
2
Colour
Convert RGB → YUV colour space
3
Blur
Gaussian blur 3×3 to reduce noise
4
Resize
Scale to 200 × 66 pixels
5
Normalise
Divide by 255 → pixel values in [0, 1]
Augmentation (Training Only)
Random Pan
50%
Shifts image ±10% horizontally / vertically
Zoom
50%
Scales image 1.0–1.2× to vary distance
Brightness
50%
Adjusts brightness 0.4–1.2× for lighting variation
Horiz. Flip
50%
Mirrors image; steering angle is negated
⚠ Augmentation applied only to training batches — validation uses raw images for unbiased evaluation

## Slide 6
Training Configuration
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
6 / 10
Hyperparameters
Optimiser
Adam
Learning Rate
0.0001
Loss Function
Mean Squared Error
Batch Size
64
Epochs
10
Steps/Epoch
300
Validation Steps
200
Train/Val Split
80% / 20%
Google Colab Workflow
1
Mount Google Drive & extract data.7z
2
Load driving_log.csv → balance steering bins
3
80/20 train/val split
4
Batch generator with on-the-fly augmentation
5
Train CNN → plot loss curve
6
Download model.h5 to local machine
No local GPU required — all training offloaded to Colab's free GPU runtime

## Slide 7
Local Deployment — drive.py
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
7 / 10
Environment Setup
conda deactivate
Exit any existing environment
conda create -n drive_env python=3.9
Create a clean Python 3.9 env
conda activate drive_env
Activate the environment
pip install tensorflow opencv …
Install ML + utility packages
pip install python-socketio==4.6.1
⚠ Exact version for simulator
pip install python-engineio==3.13.2
⚠ Exact version for simulator
Real-Time Control Loop
1
Load Model
Rebuild architecture locally Call load_weights('model.h5')
↓
2
Start Server
Socket.IO server on port 4567 Eventlet WSGI
↓
3
Receive Frame
Simulator sends base64 encoded camera image
↓
4
Preprocess
Crop → YUV → Blur → Resize → Normalise
↓
5
Predict
model.predict() → steering angle (float)
↓
6
Send Control
Emit steering + throttle back to simulator
Throttle = 1.0 − speed / maxSpeed → car slows as it approaches speed limit

## Slide 8
Results & Evaluation
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
8 / 10
~30 FPS
Real-time inference speed
<0.03
Final validation MSE loss
10
Training epochs
Full Lap
Autonomous completion
Training Metrics
Driving Behaviour
Loss decreased steadily over all 10 epochs
No overfitting — train and val loss tracked closely
Validation MSE remained below 0.03
Data balancing reduced straight-driving bias effectively
Car completed full laps without leaving the road
Steering was smooth with no erratic oscillation
Dynamic throttle maintained stable speed in curves
Real-time inference with no noticeable lag

## Slide 9
Challenges & Solutions
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
9 / 10
Socket version conflict
⚠ Problem:
Newer python-socketio versions break the simulator protocol
✔ Solution:
Pinned python-socketio==4.6.1 & python-engineio==3.13.2 in a dedicated Conda env
Keras model load crash
⚠ Problem:
load_model() failed due to version mismatch between Colab and local Keras
✔ Solution:
Rebuilt model architecture locally in drive.py and used load_weights() instead
Straight-driving data bias
⚠ Problem:
Most collected data had steering ≈ 0, causing model to favour going straight
✔ Solution:
Histogram-based balancing capped each steering bin at 500 samples
No local GPU
⚠ Problem:
Training a CNN locally would be too slow on a standard laptop
✔ Solution:
Offloaded all training to Google Colab's free GPU runtime

## Slide 10
Self-Driving Car Simulator | Muhammad Saim Razzaq | Ahsan Nadeem | 2026
10 / 10
Conclusion
A compact NVIDIA-inspired CNN successfully learned to drive a simulated vehicle purely from human demonstration data — no hand-crafted rules, no explicit lane detection. The Colab-to-local workflow proved highly practical: cloud GPU for training, standard laptop for real-time inference.
End-to-end learning eliminates the need for a multi-stage pipeline
Data quality & balancing matter more than model complexity
Strict dependency management is critical for simulator compatibility
Google Colab enables GPU training without expensive local hardware
Future Work:
Multi-track generalisation • Left/right camera offsets • RC car deployment • Reinforcement learning
github.com/MuhammadSaim-razzaq/behavioral-cloning-self-driving